## Slide 1: ECE-777 System Level Design and Automation Introduction
Cristinel Ababei
Electrical and Computer Department, North Dakota State University
Spring 2012

## Slide 2
Outline
Syllabus, focus of this course, topics covered, project
Complex embedded systems are becoming SoCs
SoCs: characteristics, applications, complexity, concurrency, heterogeneity
VLSI design flow vs. SoC design flow
Summary

## Slide 3: Syllabus

## Slide 4: Syllabus
Topics covered
No single textbook yet, research papers
Project
HW assignments and in-class presentations
Grading
Class website
  www.dejazzer.com/ece777/index.html
BlackBoard for additional materials

## Slide 5: SoC era has come Motivation is increase of “performance”, decrease of costs and time-to-market

## Slide 6
Increasing integration:
Complex embedded systems  SoCs

## Slide 7: System-on-Chip (SoC)
SoC refers to integrating all components of an electronic system into a single chip (what motivates such integration?):
  Microprocessors, microcontrollers, DSP’s
  ASIC’s, FPGA’s
  Memories, IO’s, A/D and D/C converters
  Analog, mixed-signal, RF blocks, voltage regulators
Communication infrastructure: Bus based, Network-on-Chip (NoC).
System-level design (automation) and simultaneous optimization of numerous design metrics is key challenge.
A SoC is a complex embedded system.

## Slide 8
Embedded systems characteristics
Computational
Interact (sense, manipulate, communicate) with the external world: sensors, actuators
Reactive: at the speed of the environment
Heterogeneity: hardware/software blocks, mixed architectures
Networked: shared, adaptive, sensor networks (buildings, environmental monitoring), smart products, wearable computing
Flexibility: can run/implement multiple applications sequentially or concurrently - concurrency
Reprogrammability/reconfigurability: flexibility in upgrading, bug fixing, product differentiation, product customization
Part of a larger system (system within system)
Performance and constraints:
  Timing (frequency, latency, throughput)
  Cost, power, area, weight, temperature, reliability

## Slide 9
Key recent trends
Increasing computation demands, increasing complexity
  e.g. multimedia processing in set-top boxes, HDTV
Increasingly networked
Increasing need for flexibility
  time-to-market under ever changing standards
HW-SW co-design
Higher integration: more blocks on the same chip
IP reuse, platform based design, NoC vs. Bus
Systems are designed and built as “systems of systems”.
Diversity in design methodologies, platform dependent, lack of standards  quality risks, customer confusion

## Slide 10
SoC market size

## Slide 11
Complexity and heterogeneity
controller
control panel
Real-time
OS
controller
processes
UI
processes
ASIC
Programmable
DSP
Programmable
DSP
DSP
Assembly
Code
DSP
Assembly
Code
Dual-ported
RAM
CODEC
Complexity - handled by working at higher levels of abstraction, hierarchy
Heterogeneity - handled by sophisticated HW-SW co-design methodologies

## Slide 12: Application domains
Consumer electronics (HDTV, digital cameras, camcorders, game consoles), communications (cell phones), space, automotive (video, audio, control), military (radar, sonar), health.
More than 30% of the cost of a car is now in Electronics. 90% of all innovations will be based on electronic systems. Modern cars: up to ~100 processors running complex software.
Estimated 98% of 8 Billion CPUs produced in 2000 used for embedded apps.

## Slide 13: More applications
Read (“IP reuse” – key concept in system level design – applies to course design too):
  The Introduction presentation of ECE-249 at Berkeley:
    http://chess.eecs.berkeley.edu/design/2010/lectures/IntroductionEE249_10.pdf
  The introduction presentation of CSE-237D at UCSD:
    http://haduken.ucsd.edu/cse237d/topic01.ppt

## Slide 14: Design flows (i.e., methodologies)

## Slide 15
VLSI design flow examples

## Slide 16
SoC design flow example

## Slide 17
Example: Tensilica

## Slide 18
Example: ARM

## Slide 19
Handling heterogeneity: HW/SW co-design
Fixed Processor Architecture
Application Specific HW Block
Application-Specific Instruction Set Processor

## Slide 20: SoC design flow
Various design methodologies
  Computation centric: Bus based – past and present
  Communication centric: Network-on-Chip based – more recent
Key design steps: Intertwined subtasks
  Modeling/specification
  Refining (or “functional/structural partitioning”) : the function to be implemented into smaller, interacting pieces  hierarchy
  HW/SW partitioning: elements in the refined model to either (1) HW units, or (2) SW running on custom hardware or a suitable programmable processor
  Allocation (platform design): select components/blocks/IPs
  Binding (mapping = implementation): assign functions to HW/SW components
  Scheduling: compute the times at which the functions are executed. This is important when several modules in the partition share a single hardware unit.
  Verification & debugging
Crucial is the co-design and joint optimization of hardware and software
For NoC based approach: network synthesis step is crucial

## Slide 21: System specification, Allocation (platform design)

## Slide 22: Binding (mapping), Scheduling

## Slide 23: System level design
System-level design is a complex synthesis tasks
  software synthesis and code generation
  hardware synthesis
  interface and communication synthesis
  hardware/software partitioning and component selection
  hardware/software scheduling
Major Components:
  Application specification
  Design space exploration and system optimization
  Estimation: Synthesis based on abstraction only makes sense if there are powerful estimation methods available:
    Estimate properties of the next layer(s) of abstraction.
    Design decisions are based on these estimated properties.

## Slide 24
Hardware vs. Software Modules
A significant part of the problem is deciding which parts should be in software on programmable processors, and which in specialized hardware.
Hardware = functionality implemented via a custom architecture (datapath + FSM)
Software = functionality implemented in software on a programmable processor
Key differences:
  Multiplexing
    software modules multiplexed with others on a processor
    hardware modules are typically mapped individually on dedicated hardware
  Concurrency
    processors usually have one “thread of control”
    dedicated hardware often has concurrent datapaths

## Slide 25: Challenges
Increasing application complexity
  large systems with legacy functions
  mixture of event driven and data flow tasks
  examples: multimedia, automotive, mobile communication
Increasing target system complexity: heterogeneity  HW/SW co-design
  mixture of different technologies, processor types, and design styles
  large SoCs combining components from different sources, distributed system implementations
Design chain integration:
  Design steps role  Methodology  Tools
Parallel architectures
Embedded software and control
Numerous constraints and design objectives
  examples: cost, power consumption, timing constraints, dependability/reliability

## Slide 26
Design methodologies
Past and present:
  Ad hoc approaches based on earlier experience with similar products, and on manual design.
  HW-SW partitioning decided at the beginning, and then designs proceed separately.
Present and future:
  HW-SW co-design
  Design automation (CAD) tools: very challenging

## Slide 27: Tools, companies, academia (open-source)
Design tools provided directly by SoC vendors or EDA companies
  CAD tools for hardware
  Software development environments for software
  Implement a variety of design methodologies
SoC companies
  http://en.wikipedia.org/wiki/List_of_system-on-a-chip_suppliers
Academia examples
  http://ptolemy.eecs.berkeley.edu
  http://www.cecs.uci.edu/~gajski/tools.html
  http://vlsiarch.ecen.okstate.edu/?page_id=12
Other resources
  http://embedded.com
  http://www.design-reuse.com
  http://www.soccentral.com
  http://www.socconference.com
NoC Blog
  http://networkonchip.wordpress.com

## Slide 28
Observations
“We are in the middle of a revolution in the way electronics products are designed”
System design is the key (also for IC design!)
  Start with the highest possible level of abstraction (e.g., control algorithms)
  Establish properties at the right level
  Use formal models
  Leverage multiple “scientific” disciplines

## Slide 29: Summary
Course syllabus, topics outline
SoC era has come: characteristics & applications
Design flows
System design is the key
Emphasis in this course will be put on design automation and on NoC design paradigm
Project (with milestones) is 50% of final grade
HW #1: “15-slides” style presentation