## Slide 1: ECE-777 System Level Design and Automation Performance abstraction
Cristinel Ababei
Electrical and Computer Department, North Dakota State University
Spring 2012

## Slide 3: Performance analysis
Simulation based
  Accurate but requires long CPU runtimes
Estimation based
  Statistical and analytical methods
  Less accurate but faster (orders of magnitude sometimes)
For NoCs, we need estimation of:
  Latency, throughput
  Power (router = crossbar switch + buffers, links/wires)
  Area
  Temperature

## Slide 4: Outline
Latency, throughput
Power, area
Interconnect (wire delay)
Temperature

## Slide 5: Articles
[] Jongman Kim, Dongkook Park, Chrysostomos Nicopoulos, N. Vijaykrishnan, Chita R. Das, Design and analysis of an NoC architecture from performance, reliability and energy perspective, ANCS, 2005. (average latency, energy)
[] Umit Y. Ogras, Radu Marculescu, Analytical router modeling for networks-on-chip performance analysis, DATE, 2007. (average latency, average buffer utilization, network throughput)
[] E. Krimer et al., Packet-level static timing analysis for NoCs, NoCS, 2009. (end-to-end latency)
[] Chapter 23. William James Dally, Brian Patrick Towles, Principles and Practices of Interconnection Networks, Morgan Kaufmann, 2004.
[] Nikita Nikitin, Jordi Cortadella, A performance analytical model for Network-on-Chip with constant service time routers, ICCAD, 2009. (worst case delay)
[] Mingche Lai, Lei Gao, Nong Xiao, Zhiying Wang, An accurate and efficient performance analysis approach based on queuing model for Network on Chip, ICCAD, 2009.
…

## Slide 6: Average latency
Queuing theory
  Average network latency: actual message transfer time + blocking time
  Assumption: (header) flit arrivals at router inputs are governed by independent and identical Poisson processes
  Contention probabilities is key
Markov chain based models
  Reduced Markov chain model for individual flows

## Slide 7: Latency Estimation vs. Simulation
Kim et al. (2005)
Ogras and Marculescu (2007)
For 1000 mappings:
22 h to find best mapping via simulation
7 seconds via estimation

## Slide 8: Outline
Latency, throughput
Power, area
Interconnect (wire delay)
Temperature

## Slide 9: Articles
[] Terry Tao Ye, Giovanni De Micheli, Luca Benini, Analysis of power consumption on switch fabrics in network routers, DAC, 2002. (switch/router power)
[] Andrew Kahng, Bin Li, Li-Shiuan Peh and Kambiz Samadi, ORION 2.0: A Fast and Accurate NoC Power and Area Model for Early-Stage Design Space Exploration, DATE, 2009.
[] Hangsheng Wang, Li-Shiuan Peh and Sharad Malik, A Power Model for Routers: Modeling Alpha 21364 and InfiniBand Routers, Proceedings of Hot Interconnects 10, Stanford, CA, August 2002.
[] Jongman Kim, Dongkook Park, Chrysostomos Nicopoulos, N. Vijaykrishnan, Chita R. Das, Design and analysis of an NoC architecture from performance, reliability and energy perspective, ANCS, 2005.
[] Li Shang, Li-Shiuan Peh and Niraj K. Jha, Dynamic Voltage Scaling with Links for Power Optimization of Interconnection Networks, 9th International Symposium on High-Performance Computer Architecture (HPCA), Anaheim, CA, January 2003. (router components, physical links)
[] J. Chan, S. Parameswaran, NoCEE: energy macro-model extraction methodology for network on chip routers, ICCAD, 2005.
[] Haytham Elmiligi, Ahmed A. Morgan, M. Watheq El-Kharashi and Fayez Gebali, Power Optimization for Application-Specific Networks-on-Chips: A Topology-Based Approach, Journal of Microprocessors and Microsystems, 2009.
[] D. Brooks, R. P. Dick, R. Joseph, L. Shang, Power, Thermal, and Reliability Modeling in Nanometer-Scale Microprocessors, MICRO, 2007.
…

## Slide 10: Power estimation
What is the power consumption of different switch fabric architectures under different traffic patterns/loads?
How does the power consumption scale with different numbers of input/output ports?

## Slide 11: Challenges
Simulation based methods become very slow
Power consumption of buffers depends on the dynamic contention between packets
Power components
  Switch
  Buffers
  Wires (internal to the switch/router)
  Physical links

## Slide 12: Block diagram of a switch/router
The Bit Energy: E_bit – the summation of the energy consumed for each bit on crossbar switches, internal buffers, and interconnect wires

## Slide 13: Power: switch/router
Bit energy on switch fabrics
  Input state-dependent (e.g., switch will consume more power to process 2 packets at the same time, but power consumption is not necessarily double)
  For a router with n input ports  2^n input vectors
  One idea: use look-up tables pre-computed using for example Synopsys Power Compiler

## Slide 14: Power: buffers
Contention
  Destination contention (two or more packets requesting the same output port) – application dependent. Not considered.
  Interconnect contention (the same link is shared between packets with different destinations) – depends of architecture.
Sources of energy consumption
  Data access energy: consumed by read/write
  Refreshing energy

## Slide 15: Power: interconnects
Energy consumed when the signal on the wire will toggle between logic “0” and logic “1”
Energy dissipated in the charging and discharging process
C_wire: wire capacitance – estimated using Thompson model (as global wire estimation)
C_input: total capacitance of the input gates connected to the interconnect

## Slide 16: Interconnection fabric architectures
Crossbar switch fabrics
Fully connected network
Banyan network
Batcher-Banyan network

## Slide 17: Power consumption for different number of ports

## Slide 18: Power consumption for different switch fabric sizes and under different traffic

## Slide 19: Remarks
Interconnect contention induces significant power consumption on internal buffers, and the power consumption on buffers will increase sharply as throughput increases
For switch fabrics with a small number of ports, internal node switches dominate the power consumption. For large number of ports interconnect wires will gradually dominate the power consumption.

## Slide 20: Router power consumption
Shang et al. (2003)
TSMC 0.25 um technology

## Slide 21: Outline
Latency, throughput
Power, area
Interconnect (wire delay)
Temperature

## Slide 22: Articles
[] Luca Carloni, Andrew B. Kahng, Swamy Muddu, Alessandro Pinto, Kambiz Samadi, Puneet Sharma, Interconnect modeling for improved system-level design optimization, ASP-DAC, 2008. (wire delay, buffer delay, wire power)

## Slide 23: Key factors that delay models must address
Accuracy
  Transition time (slew) dependence
  Interconnect resistivity
  Coupling capacitance
Design styles and buffering schemes
  Wire shielding, wire sizing
  Buffering
Model inputs and technology capture
  Should be derivable from standard tech files

## Slide 24: Delay models
Repeater delay
Intrinsic delay
Drive resistance
Repeater out slew
Repeater input capacitance
Wire delay
  Scattering-aware resistivity
  Interconnect barrier

## Slide 25
Carloni et al. (2008)

## Slide 26: Outline
Latency, throughput
Power, area
Interconnect (wire delay)
Temperature

## Slide 27: Articles
[] Li Shang, Li-Shiuan Peh, Amit Kumar, Niraj K. Jha, Thermal Modeling, Characterization and Management of On-Chip Networks, MICRO, 2004.
[] Giacomo Paci, Francesco Poletti, Luca Benini, Paul Marchal, Exploring temperature-aware design in low-power MPSoCs, International Journal of Embedded Systems, 2007.
[] Srinivasan Murali et al., Temperature-aware processor frequency assignment for MPSoCs using convex optimization, ICCAD 2007.

## Slide 28: Thermal modeling of NoCs
Inter-router thermal correlation modeling
  Heat dissipation path
Inter-block thermal correlation

## Slide 29: Model validation

## Slide 30: Thermal modeling of links
Given the length of link segments, the temperature along each segment can be calculated using the following equation:

## Slide 31: Others: outline
Stochastic communication
Workload/traffic characterization

## Slide 32: Stochastic communication
Article
  [] P. Bogdan, T. Dumitras, R. Marculescu, Stochastic Communication: A New Paradigm for Fault-Tolerant Networks-on-Chip, Hindawi VLSI Design, Special Issue on Networks-on-Chip, Feb. 2007.
  …
Novel communication paradigm
  Separation between computation and communication
  Fault-tolerance
  Extremely low latency
  Low production costs
  Design flexibility
Probabilistic analysis

## Slide 33: Algorithm executed concurrently by all nodes in the network

## Slide 34: Others: outline
Stochastic communication
Workload/traffic characterization
  Reading assignment: select a paper on workload/traffic characterization and read it; be prepared to discuss it in class