## Slide 1: Selected Topics
Cristinel Ababei
Marquette University

## Slide 2: Outline
Instantiating Components
VHDL to/from Verilog

## Slide 3: Example: fourbit_adder Single Architecture
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity fourbit_adder is
port(
a, b : in STD_LOGIC_VECTOR(3 downto 0);
z : out STD_LOGIC_VECTOR(3 downto 0);
cout : out STD_LOGIC
);
end fourbit_adder;
architecture MY_STRUCTURE of fourbit_adder is
component FULL_ADDER
port(
x, y, cin : in STD_LOGIC;
sum, cout : out STD_LOGIC
);
end component;
signal c0, c1, c2, c3 : STD_LOGIC;
begin
c0 <= '0';
b_adder0: FULL_ADDER port map (a(0), b(0), c0, z(0), c1);
b_adder1: FULL_ADDER port map (a(1), b(1), c1, z(1), c2);
b_adder2: FULL_ADDER port map (a(2), b(2), c2, z(2), c3);
b_adder3: FULL_ADDER port map (a(3), b(3), c3, z(3), cout);
end MY_STRUCTURE;

## Slide 4: How to Instantiate fourbit_adder
architecture MY_STRUCTURUAL_TOP of top_level is
component fourbit_adder
port(
a, b : in STD_LOGIC_VECTOR(3 downto 0);
z : out STD_LOGIC_VECTOR(3 downto 0);
cout : out STD_LOGIC
);
end component;
signal my_a1, my_b1, my_z1 : STD_LOGIC_VECTOR(3 downto 0);
signal my_cout1 : STD_LOGIC;
signal my_a2, my_b2, my_z2 : STD_LOGIC_VECTOR(3 downto 0);
signal my_cout2 : STD_LOGIC;
begin
inst_fourbit_adder_1: fourbit_adder port map (
my_a1, my_b1, my_z1, my_cout1);
inst_fourbit_adder2: fourbit_adder port map (
z => my_z2,
a => my_a2,
b => my_b2,
cout => my_cout2);
end MY_STRUCTURUAL_TOP;
architecture MY_STRUCTURUAL_TOP of top_level is
signal my_a1, my_b1, my_z1 : STD_LOGIC_VECTOR(3 downto 0);
signal my_cout1 : STD_LOGIC;
signal my_a2, my_b2, my_z2 : STD_LOGIC_VECTOR(3 downto 0);
signal my_cout2 : STD_LOGIC;
begin
inst_fourbit_adder_1: entity work.fourbit_adder port map (
my_a1, my_b1, my_z1, my_cout1);
inst_fourbit_adder2: entity work.fourbit_adder port map (
z => my_z2,
a => my_a2,
b => my_b2,
cout => my_cout2);
end MY_STRUCTURUAL_TOP;

## Slide 5: Example: fourbit_adder More than one Architecture
library ieee;
use ieee.std_logic_1164.all;
use ieee.numeric_std.all;
entity fourbit_adder is
port(
a, b : in STD_LOGIC_VECTOR(3 downto 0);
z : out STD_LOGIC_VECTOR(3 downto 0);
cout : out STD_LOGIC
);
end fourbit_adder;
architecture MY_STRUCTURE of fourbit_adder is
component FULL_ADDER
port(
x, y, cin : in STD_LOGIC;
sum, cout : out STD_LOGIC
);
end component;
signal c0, c1, c2, c3 : STD_LOGIC;
begin
c0 <= '0';
b_adder0: FULL_ADDER port map (a(0), b(0), c0, z(0), c1);
b_adder1: FULL_ADDER port map (a(1), b(1), c1, z(1), c2);
b_adder2: FULL_ADDER port map (a(2), b(2), c2, z(2), c3);
b_adder3: FULL_ADDER port map (a(3), b(3), c3, z(3), cout);
end MY_STRUCTURE;
architecture MY_BEHAVIORAL of fourbit_adder is
signal temp : unsigned(4 downto 0);
begin
temp <= resize(unsigned(a),4) + resize(unsigned(b),4);
z <= std_logic_vector(temp(3 downto 0));
cout <= temp(4);
end MY_BEHAVIORAL;

## Slide 6: How to Instantiate fourbit_adder Use Configuration
architecture MY_STRUCTURUAL_TOP of top_level is
component fourbit_adder
port(
a, b : in STD_LOGIC_VECTOR(3 downto 0);
z : out STD_LOGIC_VECTOR(3 downto 0);
cout : out STD_LOGIC
);
end component;
signal my_a1, my_b1, my_z1 : STD_LOGIC_VECTOR(3 downto 0);
signal my_cout1 : STD_LOGIC;
signal my_a2, my_b2, my_z2 : STD_LOGIC_VECTOR(3 downto 0);
signal my_cout2 : STD_LOGIC;
begin
inst_fourbit_adder_1: fourbit_adder port map (
my_a1, my_b1, my_z1, my_cout1);
inst_fourbit_adder_2: fourbit_adder port map (
my_a2, my_b2, my_z2, my_cout2);
and MY_STRUCTURUAL_TOP;
configuration MY_CONFIGURATION of top_level is
for MY_STRUCTURUAL_TOP
for inst_fourbit_adder_1: fourbit_adder use
entity fourbit_adder(MY_STRUCTURE);
end for;
for inst_fourbit_adder_2: fourbit_adder use
entity fourbit_adder(MY_BEHAVIORAL);
end for;
end for;
end MY_CONFIGURATION;

## Slide 7: How to Instantiate fourbit_adder
architecture MY_STRUCTURUAL_TOP of top_level is
signal my_a1, my_b1, my_z1 : STD_LOGIC_VECTOR(3 downto 0);
signal my_cout1 : STD_LOGIC;
signal my_a2, my_b2, my_z2 : STD_LOGIC_VECTOR(3 downto 0);
signal my_cout2 : STD_LOGIC;
begin
inst_fourbit_adder_1: entity work.fourbit_adder(MY_STRUCTURE) port map (
my_a1, my_b1, my_z1, my_cout1);
inst_fourbit_adder2: entity work.fourbit_adder(MY_BEHAVIORAL) port map (
z => my_z2,
a => my_a2,
b => my_b2,
cout => my_cout2);
end MY_STRUCTURUAL_TOP;
The most elegant approach?

## Slide 8: VHDL vs. Verilog
See Lab #9 of this class:
  http://dejazzer.com/ee478/labs/lab9_hdmi.pdf
Download also the lab files to see VHDL vs. Verilog code:
  dejazzer.com/ee478/labs/lab9_files.zip